MIG Guideform Specifications

April 09, 2002

Machine protection, control, monitoring and metering shall be provided in one integrated digital package for application on generators and motors and suitable for incorporation in an integrated substation control system.

Protection and control functions shall include:

- Thermal image protection

- Unbalance or current reversal

- Time overcurrent elements: one for phase, one for ground

- Instantaneous overcurrent elements: one for phase, one for ground

- Time overcurrent curve characteristics: 4 pre-configured, one user configurable

- Undercurrent

- Starts/hour & time between starts

- Locked rotor

- 6 outputs, four of them configurable

- Two setting tables: one pre-configured for generators and the other one for motors

Monitoring features shall include:

- 24 event record

- Oscillography

- Per phase current metering